## Slide 1: Lab 1
Introduction to Communication System

## Slide 2: EXPERIMENT NO-1
AIM: Introduction to Spectrum analyzer (Dynamic Signal Analyzer in NI MyDAQ).
Basics of Filters and their signal output, Concept of Bandwidth

## Slide 3: Spectrum Analyzer
The electronic instrument, used for analyzing waves in frequency domain is called spectrum analyzer. Basically, it displays the energy distribution of a signal on its CRT screen. Here, x-axis represents frequency and y-axis represents the amplitude.
Types of Spectrum Analyzers
Filter Bank Spectrum Analyzer
Superheterodyne Spectrum Analyzer

## Slide 4: Block diagram of filter bank spectrum analyzer : The spectrum analyzer, used for analyzing the signals are of AF range is called filter bank spectrum analyzer, or real time spectrum analyzer because it shows (displays) any variations in all input frequencies.
It has a set of band pass filters and each one is designed for allowing a specific band of frequencies. The output of each band pass filter is given to a corresponding detector.
All the detector outputs are connected to electronic switch. This switch allows the detector outputs sequentially to the vertical deflection plate of CRO. So, CRO displays the frequency spectrum of AF signal on its CRT screen.

## Slide 5: Block diagram of superheterodyne spectrum analyzer: The spectrum analyzer, used for analyzing the signals are of RF range is called superheterodyne spectrum analyzer. Its block diagram is shown in below figure.
The RF signal, which is to be analyzed is applied to input attenuator. If the signal amplitude is too large, then it can be attenuated by an input attenuator.
Low Pass Filter (LPF) allows only the frequency components that are less than the cut-off frequency.
Mixer gets the inputs from Low pass filter and voltage tuned oscillator. It produces an output, which is the difference of frequencies of the two signals that are applied to it.
IF amplifier amplifies the Intermediate Frequency (IF) signal, i.e., the output of mixer. The amplified IF signal is applied to detector.
The output of detector is given to vertical deflection plate of CRO. So, CRO displays the frequency spectrum of RF signal on its CRT screen.

## Slide 6: Dynamic Signal Analyzer
The NI ELVISmx Dynamic Signal Analyzer (DSA) performs a frequency domain transform of the AI or Audio Input waveform measurement. It can either continuously make measurements
or make a single scan. You can also apply various window and filtering options to the signal.
This instrument has the following measurement parameters:
• Source Channel: AI 0 and AI 1; Audio Input Left and Audio Input Right
• Voltage Range:
– For AI channels: ±10 V, ±2 V
– For Audio Input channels: ±2 V

## Slide 7: Dynamic Signal Analyzer

## Slide 8: Filter
Low pass filter(LPF) – Allows low frequencies
High pass filter(HPF) – Allows high frequencies
Band pass filter(BPF) – Allows band of frequencies
Band reject filter(BRF) – Rejects band of frequencies
All pass filter – Allows all frequencies but with a phase shift
A filter is a circuit capable of passing (or amplifying) certain frequencies while attenuating other frequencies. Thus, a filter can extract important frequencies from signals that also contain undesirable or irrelevant frequencies.

## Slide 9: Types of filter:

## Slide 10: Types of filter:

## Slide 11: Passive Low Pass Filter
In low frequency applications (up to 100kHz), passive filters are generally constructed using simple RC (Resistor-Capacitor) networks.
while higher frequency filters (above 100kHz) are usually made from RLC (Resistor-Inductor-Capacitor) components.
Passive filters are made up of passive components such as resistors, capacitors and inductors and have no amplifying elements (transistors, op-amps, etc.) so have no signal gain, therefore their output level is always less than the input.

## Slide 12: Example-1) A Low Pass Filter circuit consisting of a resistor of 4k7Ω in series with a capacitor of 47nF is connected across a 10v sinusoidal supply. Calculate the output voltage ( VOUT ) at a frequency of 100Hz and again at frequency of 10,000Hz or 10kHz.

## Slide 14: Transfer Function consider same example-1

## Slide 15: Requirement: MATLAB Simulink

## Slide 16: MATLAB Simulink

## Slide 17: MATLAB Simulink

## Slide 18: F= 100Hz, Vout= 9.9v

## Slide 19: Optional: On Multisim:

## Slide 20: F= 200Hz

## Slide 21: F=300

## Slide 22: On Multisim

## Slide 23: F= 400

## Slide 24: F= 500Hz

## Slide 25: F=600

## Slide 26: F=700

## Slide 27: F=800

## Slide 28: F=900

## Slide 29: F=1000

## Slide 30: On Multisim

## Slide 31: F=5000

## Slide 32: F= 10,000Hz Vout= 0.718

## Slide 33: RC LPF on Multisim When input voltage is 10V at 10KHz frequency Vout=0.5065

## Slide 34: Voltage Output at a Frequency of 10,000Hz (10kHz).

## Slide 35: Frequency Response
We can see from the results above, that as the frequency applied to the RC network increases from 100Hz to 10kHz, the voltage dropped across the capacitor and therefore the output voltage ( VOUT ) from the circuit decreases from 9.9v to 0.718v.
By plotting the networks output voltage against different values of input frequency, the Frequency Response Curve or Bode Plot function of the low pass filter circuit can be found, as shown below.

## Slide 36: Cut-off Frequency and Phase Shift
Then for our simple example of a “Low Pass Filter” circuit above, the cut-off frequency (ƒc) is given as 720Hz with an output voltage of 70.7% of the input voltage value and a phase shift angle of -45o.
It means that RC LPF will block the signal with 720 Hz or more
Signals with 720 Hz and below will pass easily through the filter.

## Slide 37: Frequency Response of a 1st-order Low Pass Filter
Ref: [1]

## Slide 38: Example 2- Transfer Function:
= 1/0.01
Consider,
R = 10 KΩ and C= 1 microfarad for RC LPF calculate T.F=?

## Slide 39: Input frequency: 1 Hz

## Slide 40: Parameters for TF:

## Slide 41: R= 10Kohm, c=1microfarad,Vin 10 V, Frequency= 1Hz
Xc = 159154.94
Vout = 10 x 0.998 = 9.98v

## Slide 42: When the frequency is 1Hz Output voltage approximately 10V

## Slide 43: R= 10Kohm, c=1microfarad,Vin 10 V, Frequency= 10Hz
Xc = 15915.494
Vout = 10 x 0.8467 = 8.467v

## Slide 44: When the frequency is 10Hz Output voltage = 8.467V

## Slide 45: R= 10Kohm, c=1microfarad,Vin 10 V, Frequency= 100Hz Vout=?

## Slide 46: Cut-off frequency:
= 1/ 2*pi* 10K*1microfarad
Fc = 15.91 Hz
It means that RC LPF will block the signal with 15.91 Hz or more
Signals with 15.91 Hz and below will pass easily through the filter.

## Slide 47: References:
[1] https://www.electronics-tutorials.ws/filter/filter_2.html
[2]https://www.tutorialspoint.com/electronic_measuring_instruments/electronic_measuring_instruments_spectrum_analyzers.htm
[3] https://www.allaboutcircuits.com/technical-articles/an-introduction-to-filters/
[4] https://www.youtube.com/watch?v=MNcu3TfPPQ8
[5] https://resources.pcb.cadence.com/blog/2021-simplify-rlc-circuit-analysis-with-the-rlc-transfer-function
[6] https://www.youtube.com/watch?v=zsnXcKj1MBc
[7] “B.P.Lathi”, Modern Digital and Analog Communication Systems Page no. 104,105

## Slide 48
Thank you